## Slide 1
DIGITAL ELECTRONICS PROJECT · SECTION 12
Half Adder,
Full Adder &
4-Bit Arithmetic Unit
From basic gates to an unsigned ripple-carry adder.
JOSHITH NVS PERUGU — 2620030096
POTNURU RISHITH KUMAR — 2620030126
R YAGNA CHARAN — 2620030129
CHIGULAPALLY VINEETH — 2620030155
4-BIT ADDER · OVERVIEW
A[3:0]
B[3:0]
FA0
FA1
FA2
FA3
S[3:0]
C4
Inputs → repeated full adders → sum and carry-out
Notes: This project moves from one-bit addition to a complete four-bit unsigned ripple-carry arithmetic unit. The circuit is built from basic gates, then verified with representative binary inputs.

## Slide 2
DESIGN OBJECTIVE
From one-bit addition to a 4-bit arithmetic unit
The same two outputs repeat at every bit position: a sum bit and a carry bit.
OBJECTIVE
Design half adders and full adders from basic gates, then cascade full adders to perform 4-bit binary addition. XOR produces the sum bit while AND/OR networks propagate carry.
OUTCOME
The modular unit accepts A3–A0 and B3–B0 and produces S3–S0 plus a final carry-out.
A input
B input
BASIC GATES
XOR · AND
OR network
SUM
CARRY
S3–S0
C4
Notes: We begin with the one-bit behavior. XOR determines whether the two inputs differ, while AND and OR networks carry a result into the next bit position. Repeating this structure creates a four-bit unit.

## Slide 3
GATE-LEVEL LOGIC
Half adder and full adder logic
Half adder
S = A ⊕ B; C = A ∧ B
Full adder
S = A ⊕ B ⊕ Cin
Cout = (A ∧ B) ∨ (Cin ∧ (A ⊕ B))
HALF-ADDER · TRUTH TABLE
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
FULL-ADDER · CIN = 0
A | B | S | Cout
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
FULL-ADDER · CIN = 1
A | B | S | Cout
0 | 0 | 1 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 1
A
B
XOR
Sum
Carry
A
B
Cin
HA1
HA2
Sum
OR
Cout
Notes: The half adder handles two input bits. A full adder adds a third input, Cin, which arrives from the previous stage. Two half adders expose the intermediate XOR result and the two carry conditions; the OR gate combines those conditions. The intermediate sum from HA1 feeds HA2; the OR combines the carry outputs.

## Slide 4
CASCADE ARCHITECTURE
Four full adders become a ripple-carry arithmetic unit
Each stage adds one pair of bits and passes its carry to the next stage.
A[3:0]
B[3:0]
FA0
A0 + B0
Cin = 0
FA1
A1 + B1
Cin = C1
FA2
A2 + B2
Cin = C2
FA3
A3 + B3
Cin = C3
C1
C2
C3
S0 LED
S1 LED
S2 LED
S3 LED
C4
FA0 connects the least-significant bits with Cin = 0. The chain then carries C1 → FA1, C2 → FA2, and C3 → FA3. Read S0–S3 as the result; C4 indicates a carry beyond the most significant bit.
Notes: This is the Logisim-style implementation view. The least-significant stage starts with zero carry-in. Every later full adder waits for the previous carry, which is why this architecture is called ripple-carry.

## Slide 5
SIMULATION CHECK
Simulation results verify the 4-bit addition
LOGISIM-STYLE STATES
0000 + 0000 → 0000 · C4 = 0
0101 + 0011 → 1000 · C4 = 0
1111 + 0001 → 0000 · C4 = 1
CARRY PATH · 1111 + 0001
FA0
FA1
FA2
FA3
Highlighted carry path
C1 → C2 → C3 → C4 = 1
Four-bit sum: 0000 · final carry beyond the word: C4 = 1
A | B | S | C4
0000 | 0000 | 0000 | 0
0101 | 0011 | 1000 | 0
1111 | 0001 | 0000 | 1
The circuit performs binary addition correctly. Ripple carry determines the propagation delay because each stage depends on the carry from the stage before it.
Notes: These three test cases exercise the basic path, an internal carry, and a carry beyond the four-bit word. The final example is especially important: zero is the four-bit sum, while C4 records the overflow beyond the most significant bit.

## Slide 6
TAKEAWAY
Conclusion: a modular adder with wide digital applications
CORE RESULT
Two half adders and an OR gate form a full adder. Four full adders form a working 4-bit unsigned ripple-carry arithmetic unit.
APPLICATIONS
ALUs, counters, address generation, digital signal processing, calculators, and processor datapaths.
NEXT IMPROVEMENTS
Use carry-lookahead logic for faster addition, add subtraction through XOR-controlled input inversion, and extend the design to wider word sizes.
MODULAR BLOCK DIAGRAM
A[3:0], B[3:0]
↓
4 × FULL ADDER
ripple-carry core
↓
S[3:0]
C4
Unsigned output word + final carry
Notes: The architecture is modular: the full adder is the reusable building block, and the four-bit unit is a direct cascade. Faster carry logic, controlled inversion for subtraction, and wider word sizes are natural next steps.